## Slide 1: Intro to Power Supplies
Mark Anderson
Project Engineer
Design Lab
12/2008

## Slide 2: Typical Power Sources
Output Type | Type
Single Voltage (single ended) | Fixed
Dual Voltage (dual output – the two outputs are equal but opposite) | Variable
Triple Voltage (usually a single ended with a dual in the same package) | 

## Slide 3: The Details
Batteries are examples of single voltage fixed supplies
Supplies may be either “grounded” or “floating”
  Grounded supplies may have either the positive or negative output grounded to the chassis
  Floating supplies have neither positive nor negative output grounded
Grounded supplies typically have these terminals:
  Red (positive)
  Black (negative)
Floating supplies typically have these terminals:
  Red (positive)
  Black (negative)
  Green (ground / chassis))
Use a meter to verify whether your supply is grounded or floating!

## Slide 4: Q&A
Question | Answer
My power supply has three terminals – red, black and one labeled “COM”. How do I use these? | This is a dual output supply. The supply provides both a positive and negative voltage with respect to the common (COM) terminal. The positive voltage is available between the red and common terminals. The negative output is available between the common and black terminals. When commercially made, these are typically floating supplies – meaning that the common terminal is NOT connected to the chassis ground. You may need to make that connection between common and ground yourself.

## Slide 5: Q&A
Question | Answer
My power supply has two other terminals labeled “S+” and “S-” -- what are those? | These are “sense” inputs to the supply. Generally they can be left disconnected or the S+ can be jumpered to the “+” terminal and the S- can be connected to the “-”. For high accuracy applications at high currents, you connect a second pair of wires from these terminals directly to your load device. These allow the supply to “sense” the actual voltage at the load, which then allows it to compensate for the voltage drop across the length of the conductors.

## Slide 6: Q&A
Question | Answer
I need 5 volts for part of my circuit and both +12 and -12 volts for another part of my circuit. What do I do? | You need a power supply system with three outputs. You need two separate supplies – a single ended and a dual output. These may be available as two independent supplies in a single package. One supply will have a single ended output set for 5 volts. The other is a dual supply which you should set for 12 volts. If your +5 and +/- 12 circuits share a common ground then be sure to connect the -5 terminal to the common terminal and for safety, connect that to the green chassis ground terminal on the power supply.