## Slide 1: Example Capstone Drawing Package
This PowerPoint is excerpted from a drawing package produced by a Capstone Design team.
It has been annotated with
  Explanation/notes on what is present
  Mistakes which should have been corrected

## Slide 2
Item Numbers
x 8
x 2
x 2
x 8
x 8
What is material?
What style head on screw?
Bill of Materials
Include columns for
manufacturer and part #
for purchased parts
Unnecessary to label each instance of part
Exploded Assembly View
Isometric View
Title Block
with meaningful part name
Bill of Materials
x 2
Quantity

## Slide 3
Cross Section View
x 2
x 2
Centerline is correct way to convey information in these notes
Standard Orthographic views - Front, Right, Top
Plus Cross section for display of offset dimension
Section Labels should be consecutive (this package is missing some pages)
Sheet scale too small
Orthographically projected sectional views must be same scale and aligned with their parent view. If they need to be larger, your sheet scale needs to increase.
Hidden lines should be shown in orthographic views.

## Slide 4
1
Item # from BOM
4” REF
Inappropriate note. Provide reference dimensions for stock material on drawing views. Unless required, no need to list vendor on print.
1/4” REF
4” REF
Per tolerance block, 3 decimal places means ±0.005” and would require milling both sides. 2-1/2” can be produced with tape measure and band saw. Time is money, so dimension and tolerance to produce required accuracy
Hidden lines can be shown to improve clarity of blind holes
If intent is to drill on center, simply draw centerline
Hole callout with thread size, depth, number of holes
Stock material is shown with reference dimensions. Machinist not expected to produce this size, but shown dim helps to verify material is correct size

## Slide 5
3
Standard Orthographic views - Front, Right, Top
Plus Back view to detail holes within step
Axonometric view
Is 3 decimal place round profile required, or would “break all corners” suffice for this application?
Incorrect hatch style for steel
Hidden lines should be shown in orthographic views.

## Slide 6
4
REF
REF
REF
Dimensions are not to be machined, simply reference for assembler to verify part. Using parentheses around the dimensions is also sufficient, e.g. (R1.498).
Include manufacturer, part #, vendor
for purchased parts
Hidden lines should be shown in orthographic views.

## Slide 7
5
Sheet scale too small

## Slide 8
6
Is high tolerance necessary? May not be possible on purchased part. Or at greatly increased price.
Required magnetic strength should be specified
Sheet scale too small

## Slide 9
8
Artifact line segment can confuse reader
Difficult to machine part based on this dimension. Simpler to dimension vertical location of arc centerpoint.
Sheet scale too small
Hidden lines should be shown in orthographic views.

## Slide 10
10
View is reversed from standard projections, protrusion should face to right based on other Front and Back views
Sheet scale too small

## Slide 11
x 4
x 4
If bolt torque is important to assembly or function, call out here
Sheet scale too small

## Slide 12
Use two sheets for two separate parts
Standard view layout and alignment not followed here
Hidden lines missing in orthographic view
Author Info MISSING

## Slide 13
Standard view layout and alignment not followed. Upper right should be axonometric view.

## Slide 14
Stacked Dimensions not appropriate. Use baseline dimensioning instead.
Standard view layout and alignment not followed. Upper right should be axonometric view.

## Slide 15
Standard view layout and alignment not followed. Upper right should be axonometric view.
Centerlines & Center marks necessary to convey important dimensions and relationships (e.g. symmetry)
Not the correct hatch pattern for Steel
Baseline dimensioning used
Stacked Dimensions not appropriate. Use baseline dimensioning instead.