## Slide 1: PSoC® 4 BLE Introduction to BLE System Design BLE = Bluetooth Low Energy PSoC = Programmable System-on-Chip
Easily Design Low-Power, Wireless Systems for the Internet of Things With the Most Integrated One-Chip BLE Solution
Patrick Kane
Director, Cypress University Alliance
pkx@cypress.com

## Slide 2: The Internet of Things Revolution
The Internet of Things (IoT) is now a commercial reality
The IoT is how everyday physical objects are connected to the Internet e.g., a thermostat is adjusted by a cell phone
Six billion everyday physical objects will be connected to the IoT by 20201
Sensor-based systems connect the “real world” to the IoT
Sensor-based IoT systems operate interactively and autonomously, typically using wireless communication
Sensor-based IoT systems must be low power to run on batteries
BLE is the de facto low-power wireless standard for the IoT
1.2 billion Bluetooth Smart Ready products were sold in 20132, including Galaxy, iPad, and Thinkpad
BLE is designed for low-power, sensor-based products like wearable electronics, medical devices and home automation devices
IoT products require sensor-based BLE systems
1 Cisco CEO John Chambers speaking at the 2014 Mobile World Congress trade show
2 ABI Research
Fitness Monitor by Jawbone
Kevo Deadbolt by Kwikset
Heart Rate Monitor by Mio

## Slide 3: Terms You Will Hear Today
Analog Front End (AFE)
  An analog signal conditioning circuit that uses opamps, filters and comparators to interface to an ADC
Balun
  An electrical device that converts a differential RF signal to a single-ended signal or vice-versa
Antenna Matching Network (AMN)
  An RLC circuit network that provides Balun functionality, antenna impedance matching and low-pass filtering
BLE Protocol Stack (BLE Stack)
  Firmware implementing the Bluetooth 4.0/4.1 specification to provide BLE communication
A typical signal path’s AFE features an opamp that drives the ADC, RC filter and the microcontroller or DSP
AMN for TI MCU (with a note for the 3rd party Chip Balun)
Bluetooth 4.1 specification
7 volumes, 2,684 pages

## Slide 4: Bluetooth Terms
Bluetooth Classic
  A legacy standard for personal area networks made popular by audio streaming to cell phone headsets
  Operated in the 2.4-GHz ISM1 band with GFSK2 modulation and supports up to 3-Mbps data rate
Bluetooth Low Energy (BLE)
A standard for short-range, low-power wireless applications that communicate state or control information
Operates in the 2.4-GHz ISM1 band with GFSK2 modulation and supports a 1-Mbps data rate
Not backward-compatible with Bluetooth Classic
Bluetooth 4.0
An upgraded Bluetooth Classic specification that adds BLE
Bluetooth 4.1
An enhanced Bluetooth 4.0 specification, adopted in Dec. 2013
Includes improved security, lower power and higher throughput3
Bluetooth Smart
A brand for Bluetooth 4.0/4.1 products that support only BLE
Bluetooth Smart Ready
A brand for Bluetooth 4.0/4.1 products that support both Bluetooth Classic and BLE
Sensor Data
Bluetooth Smart Ready Product
Bluetooth Smart Product
Bluetooth Classic
Product
Audio Streaming
1 An Industrial, Scientific, Medical (ISM) RF frequency band that is license-free worldwide
2 Gaussian frequency shift keying
3 272 Kbps (15% higher vs. 4.0) with protocol overhead
V

## Slide 5: BLE Architecture Overview
The BLE Architecture consists of three parts: Controller, Host and Application
The controller is the radio and hardware to support the transmission and reception of packets. The controller interfaces with the outside world through an antenna and to the host via the Host Controller Interface.
The host is the software stack that manages how two or more devices communicate with one another and how several different services can be provided at the same time via the controller.
The application is firmware that communicates via the host and therefore the controller to enable a use case—such as a wearable health monitoring application.
PSoC 4 BLE is a one-chip solution that integrates all three parts of the BLE Architecture.
BLE Architecture
Host
Application
Controller
Profile: HID, HRM, Glucose Meter, etc. | 
Generic Access Profile (GAP) | 
Generic Attribute Protocol (GATT) | 
Attribute Protocol (ATT) | Security Manager (SM)
Logical Link Control and Adaption Protocol (L2CAP) | 
Host Control Interface (HCI) | 
Link Layer (LL) | Direct Test Mode (DM)
Physical Layer (PHY) | 
PSoC 4 BLE Provides a One-Chip BLE Solution1
1 Refer to the Appendix for definitions of all BLE architecture terms.
Source for terms and definitions: Bluetooth Low Energy: The Developer’s Handbook
PSoC 4 BLE One-Chip Solution

## Slide 6: BLE Architecture Key Terms
Generic Access Profile (GAP)
  Defines how devices discover, connect and present useful information to the user and other devices.
  Operates in one of four roles:
  Peripheral: Connectable and operates as a slave
  Central: Initiates connections and operates as a master
  Broadcaster: Advertises but is non-connectable
  Observer: Listens and scans only
Generic Attribute Profile (GATT)
  Defines what type of data can be read or written and how that data is used.
  Operates in one of two roles:
  Client: A device that wants data
  Server: A device that has the data
  Profiles
  Specifications that standardize access profiles and attribute profiles thereby guaranteeing application-level interoperability between devices that support the same profiles. Example SIG2-supported profiles include: Heart Rate Monitor (HRM) Alert Notification Profile Health Thermometer Profile
BLE Architecture
Host
Application
Controller
Profile: HID, HRM, Glucose Meter, etc. | 
Generic Access Profile (GAP) | 
Generic Attribute Protocol (GATT) | 
Attribute Protocol (ATT) | Security Manager (SM)
Logical Link Control and Adaption Protocol (L2CAP) | 
Host Control Interface (HCI) | 
Link Layer (LL) | Direct Test Mode (DM)
Physical Layer (PHY) | 
BLE Architecture1
1 Refer to the Appendix for definitions of all BLE architecture terms.
  2 Bluetooth Special Interest Group
Source for terms and definitions: Bluetooth Low Energy: The Developer’s Handbook

## Slide 7: BLE Application Example
BLE communication between two devices:
  A Bluetooth Smart-Ready mobile phone is paired with a Bluetooth Smart fitness monitor
Profile | HRM | Scans Services
GAP Role | Central | Initiates physical link connection
GATT Role | Client | Wants data
Exposes Services | Profile | HRM
Accepts physical link connection | GAP Role | Peripheral
Has data | GATT Role | Server
Bluetooth Smart-Ready Mobile Phone
Bluetooth Smart Fitness Monitor
BLE Protocol Stack on Mobile App
BLE Protocol Stack on Fitness Monitor
BLE Connection
HRM Profile specified attributes include:
Heart Rate Measurement
Body Sensor Location
Heart Rate Control Point
Notes: The following combination of multiple roles simultaneously:
Peripheral + Broadcaster
Peripheral + Observer
Central + Broadcaster
Central + Observer

## Slide 8: RF Design Problem
  Designing wireless sensor-based systems for the IoT is difficult
  RF board design is complicated
  Designing wireless sensor-based systems requires engineers to work with design tools from multiple IC vendors
  Wireless specs require complex firmware development (e.g., the BLE Protocol Stack)
To Antenna (50 )
or
SMA (50 )
C1
18 pF
C3
18 pF
C2
1 pF
C4
1 pF
L4
2 nH
L1
2 nH
L2
1 nH
L3
3 nH
C5
1 pF
Ant 1
Ant 2
Typical AMN
Requires 9 external components
Bluetooth Specification 4.1
7 volumes, 2,684 pages

## Slide 9: PSoC 4 BLE Simplifies RF Board Design
Designing an AMN is non-trivial
  AMNs are sensitive to PCB layout and parasitics
  Tuning the AMN is required for best RF performance
  AMN tuning complexity increases dramatically when many external components are required
  A typical AMN has 7-9 external components vs. two for the Cypress AMN because the Balun is integrated
Cypress’s AMN
Vendor A’s AMN example
Vendor B’s AMN example
The PSoC 4 BLE integrated Balun simplifies RF board design and reduces PCB footprint
2 external components
7 external components
9 external components
Ant
C1
1.2 pF
L1
6.8 nH
L1
C1
18 pF
RFP
3 nH
18 pF
C3
C2
1 pF
C4
1 pF
L4
2 nH
L2
1 nH
L3
C5
1 pF
RFN
2 nH
VDD_PA
C2
1.0 pF
L3
3.3 nH
L1
4.7 nH
L2
10 nH
C1
2.2 nF
RFP
RFN
C3
2.2 pF
C4
1.5 pF

## Slide 10: PSoC 4 BLE Enables Low-Power Wireless Systems
  PSoC 4 BLE has best-in-class low-power modes
Consumes lowest current in Stop mode with I/O retention
Retains SRAM data in Hibernate mode
Retains complete system status in Deep-Sleep mode
Provides APIs to switch easily between power modes
Consumes avg. 26-μA for a 1-sec connection interval
  To learn more, download AN92584:
PSoC 4 BLE Measuring Power Consumption
Power Mode | Current Consumption | Code Execution | Digital Peripherals Available | Analog Peripherals Available | Clock Sources Available | Wake-Up Sources | Wake-Up Time
Active | 2.5 mA @ 6 MHz | Yes | All | All | All | - | -
Sleep | 1.3 mA | No | All | All | All | Any interrupt source | 0
Deep-Sleep | 4.3 μA | No | WDT1, LCD2, I2C/SPI, Link-Layer3 | Comparator, Opamps, POR4, BOD5 | WCO6, 32-kHz ILO7 | Comparator, GPIO8, WDT, SCB9 | 25 μs
Hibernate | 150 nA | No | No | Comparator, POR, BOD | No | Comparator, GPIO | 2 ms
Stop | 20 nA | No | No | No | No | Wake-Up pin, XRES10 | 2 ms
1 Watchdog timer 4 Power-on-reset
2 Liquid crystal display 5 Brownout-detect 7 32-kHz internal low-speed oscillator 9 Serial communication block
3 Digital logic managing BLE protocol 6 32-kHz watch crystal oscillator 8 General-purpose input/output 10 External reset
PSoC 4 BLE Current Consumption
20
18
16
14
12
10
8
6
4
2
0
Stage | Power Mode | Activity
A | Active | Oscillator Startup
B | Sleep | Oscillator Startup
C | Sleep | RF Transmit
D | Sleep | RF Receive
E | Active | Stack Processing
F | Deep-Sleep | WCO On
Average current consumption for connection interval of 1 sec = 18.9 µA
Deep-Sleep
Active
Sleep
Active
Current (mA)
Time (µs)
1,000
2,000
3,000
4,000
999,000
1,000,000
0
A
B
C
D
E
F
Notes: BU Note: Connection interval is a BLE spec, ranging from 7.5ms to 4s. It determines the intervals at which a master device initiates an exchange of data with a slave device.
A 1-sec connection interval is the most typical use case for applications like HRMs & pedometers. A 5-min connection interval is out of spec for BLE.
We have added numbers for the relaxed, 4s connection interval BLE spec to the competitive slide.

## Slide 11: PSoC Terms
PSoC Creator™
PSoC 3, PSoC 4 and PSoC 5LP Integrated Design Environment (IDE)
Software that installs on your PC that allows:
Concurrent hardware and firmware design of PSoC systems, or
Hardware design followed by export to popular IDEs
Components
Free embedded ICs represented by an icon in PSoC Creator software
Used to integrate multiple ICs and system interfaces into one PSoC
Dragged and dropped as icons to design systems in PSoC Creator
Inherently connected to the MCU via the main system bus
The BLE Component creates Bluetooth Smart products in minutes
The Programmable Analog Components are used for sensors
Component Configuration Tools
Simple graphical user interfaces in PSoC Creator
Embedded in each Component
Used to customize Component parameters
Accessed by right-clicking a Component
Application Programming Interfaces (API)
  Simplified set of instructions used to interact with a Component
  Reduces the firmware complexity of a design
75+ Components available
BLE Component creates Bluetooth Smart products
Programmable Analog Components create sensor interfaces

## Slide 12: PSoC Terms
PSoC 4 BLE
A PSoC 4 IC with an integrated BLE radio
Includes a royalty-free BLE Protocol Stack compatible with Bluetooth 4.1
Bluetooth Low Energy Subsystem (BLESS)
A hardware system that consists of the BLE link layer, digital physical layer (PHY) and the RF transceiver
CapSense®
Cypress’s touch-sensing user interface solution
The industry’s No. 1 solution in sales by 4x over No. 2
Universal Digital Block (UDB)
PSoC programmable digital logic block containing:
Two programmable logic devices (PLDs)
One programmable data path with an arithmetic logic unit
Status and control registers
Configured with PSoC Creator using: 1) PSoC Creator Components, 2) the graphical state machine editor, or
3) Verilog code
Continuous Time Block (CTBm)
Programmable analog block used to implement opamps, PGAs, comparators, etc.

## Slide 13: PSoC 4 BLE Integrates Programmable AFEs, Digital Logic and CapSense
Sports and fitness monitors, wearable electronics, medical devices, home automation solutions, game controllers, sensor-based low-power systems for IoT
32-bit MCU subsystem
48-MHz ARM® Cortex™-M0 CPU
Up to 256KB flash and 32KB SRAM
Programmable AFE
Four opamps, configurable as PGAs, comparators, filters, etc.
One 12-bit, 1-Msps SAR1 ADC
CapSense® with SmartSense™ Auto-tuning
One Cypress Capacitive Sigma-Delta™ (CSD) controller with
touchpad capability
Programmable digital logic
Four Universal Digital Blocks (UDB2s): custom digital peripherals
Four configurable TCPWM3 blocks: 16-bit timer, counter or PWM
Two configurable serial communication blocks (SCB4s):
I2C master or slave, SPI master or slave, or UART
Packages
56-pin QFN (7 x 7 x 0.6 mm), 68-ball CSP (3.9 x 3.5 x 0.55 mm)
Bluetooth Smart connectivity with Bluetooth 4.1
2.4-GHz BLE radio with integrated Balun
Sampling: Now
Production: 128KB Now, 256KB Q2 2015
Datasheet: PSoC 4 BLE Datasheet
Applications
Features
Collateral
Block Diagram
Availability
1 Successive approximation register 3 Timer, counter, pulse-width modulator; configurable as 16-bit timer, counter, pulse-width modulator blocks
2 Universal Digital Block 4 Serial communication block configurable as I2C/SPI/UART
Flash (256KB)
SRAM
(32KB)
Serial Wire Debug
Programmable Interconnect and Routing
GPIO x8
PSoC 4 BLE
CORTEX-M0
48 MHz
Programmable Digital
Blocks
SCB4 x2
TCPWM3 x4
UDB2 x4
SAR1 ADC
Programmable Analog Blocks
Opamp x4
CMP
x2
I/O Subsystem
MCU Subsystem
Segment LCD Drive
GPIO x8
GPIO x8
GPIO x8
GPIO x4
Advanced High-Performance Bus (AHB)
CSD
BLE Subsystem

## Slide 14: PSoC 4 BLE One-Chip Solution
PSoC 4 BLE
  1. Integrates programmable AFEs and digital logic, CapSense and an ARM Cortex™-M0 CPU with a BLE radio
  2. Delivers five flexible, easy-to-use, low-power modes
  3a. Simplifies RF board design by integrating the Balun
  3b. Enables complete system design in PSoC Creator
  3c. Simplifies the BLE Protocol Stack and BLE Profile1 configuration with the easy-to-use BLE Component
Integrate AFEs, digital logic, CapSense and an ARM Cortex-M0 with a BLE radio…
AFE ICs + BLE MCU + Stack
Dual-Channel Opamp
BLE MCU
BLE 4.1 Spec
Instrumentation Amplifier
Complete BLE System Design in PSoC Creator
And complete your system design easily using PSoC Creator and PSoC Components…
To create your PSoC 4 BLE
one-chip solution for the IoT
PSoC 4 BLE One-Chip Solution
1 A Bluetooth specification that guarantees application-level interoperability between devices that use the same Profile
VREF_IN
Electrode1
VREF
Electrode2
Opamp1
Opamp2
Opamp3
VREF
Opamp4
SARADC
VREF2
VREF_IN2
Accelerometer
CapSense
BLE

## Slide 15: Bluetooth Low Energy Pioneer Kit
The $49 BLE Pioneer Kit (CY8CKIT-042-BLE) contains:
BLE Pioneer Baseboard
Provides access to all PSoC 4 BLE GPIOs
Is compatible with Arduino™ and Digilent® Pmod™ hardware ecosystems
Features on-board CapSense slider, RGB LED, push buttons and Cypress F-RAM
Includes on-board PSoC 5LP for program and debug (KitProg)
Supports 1.9 V, 3.3 V or 5 V, including coin-cell battery operation
BLE Modules (2):
Contains two FCC-certified1 BLE modules that plug into the BLE Pioneer Baseboard
Features on-board PCB antenna and provide access to all GPIOs
Supports BLE-UART bridge via an on-board four-pin header
BLE USB Dongle
Enables a PC to act as the BLE host for developing and debugging BLE peripherals
Features an on-board LED, push button and KitProg for program and debug
Example Projects
Demonstrates how to use PSoC Creator to implement common BLE profiles, such as Heart Rate Monitor (HRM), Glucose Meter and Human Interface Device (HID)
Includes iOS and Android mobile apps with full source code
BLE Pioneer Baseboard
PSoC 4 BLE Module
BLE USB Dongle
Example iOS and Android Apps
1 A mark on electronic products manufactured or sold in the U.S. certifying that its electromagnetic interference
is under limits defined by the Federal Communications Commission
Dimensions: 28 mm x 46 mm
FCC-Certified
PCB Antenna

## Slide 16: BLE Pioneer Baseboard and PSoC 4 BLE Module
BLE Pioneer Baseboard
PSoC 4 BLE Module
CapSense® Slider
KitProg:
PSoC 5LP-based
Programmer
and Debugger
Diligent Pmod™ Compatible I/O Header
Ardunio™ Compatible I/O Header (J1 and J2)
Status LED
Power LED
Ardunio™ Compatible I/O Header (J3 and J4)
PSoC 5LP I/O Header (J8)
USB Connector (J13)
Proximity Header (J14)
Push Button
BLE Reset Button
RGB LED
BLE Module Header (J10 and J11)
System Power
Supply Jumper
(J16)
LDO 5V-1.9V
PSoC 4 BLE
CY8C4247LQI-BL483
PCB Wiggle Antenna (for BLE Radio)

## Slide 17: References and Links
  Product Webpages:
  Cypress’s BLE solutions webpage: www.cypress.com/BLE
  PSoC 4 BLE Product webpage: www.cypress.com/PSoC4BLE
  PSoC 4 BLE Product datasheet: www.cypress.com/PSoC4BLEDatasheet
  PRoC BLE Product webpage: www.cypress.com/PRoCBLE
  PRoC BLE Product datasheet: www.cypress.com/PRoCBLEDatasheet
  PSoC family roadmap: www.cypress.com/PSoCRoadmap
  PSoC Creator IDE: www.cypress.com/PSoCCreator
  BLE Pioneer Kit: www.cypress.com/CY8CKIT-042-BLE
  Application Notes:
  Getting Started with PSoC 4 BLE (AN791267): www.cypress.com/go/AN91267
  Available Q115: PSoC 4 BLE Measuring Power Consumption (AN92584): www.cypress.com/go/AN92584
  Available Q115: Creating BLE Applications Using PSoC 4 BLE (AN91184): www.cypress.com/go/AN91184
  Available Q115: Creating Custom Profiles Using PSoC 4 BLE (AN96112): www.cypress.com/go/AN96112
  Design Guides:
  PSoC 4 BLE Antenna Design Guide: www.cypress.com/go/AN91445
  CapSense Design Guide: www.cypress.com/go/AN85951
  BLE Frequently Asked Questions (FAQ): http://www.cypress.com/PSoC4BLEKBA
  BLE Compliance and Interoperability Report: www.cypress.com/BLECompliance
  Bluetooth SIG website: www.bluetooth.org
  Bluetooth Low Energy - The Developer’s Handbook, Robin Heydon: ISBN-10:013288836X

## Slide 18: General Online Resources
  BLE: www.cypress.com/BLE
  PSoC 4 BLE: www.cypress.com/PSoC4BLE
  PRoC BLE: www.cypress.com/PRoCBLE
  PSoC: www.cypress.com/PSoC
  Kits: www.cypress.com/kits
  PSoC Creator: www.cypress.com/Creator
  Support: www.cypress.com/support
  Training: www.cypress.com/training
  Cypress Store: www.cypress.com/store
  Community & forums: www.cypress.com/forums
  Application Notes: www.cypress.com/AppNotes
Cypress BLE Solutions: www.cypress.com/BLE
Cypress’s BLE solutions webpage is your one-stop-shop for everything BLE, including, Product Datasheets, Development Kits, Application Notes, Software Downloads, Example Projects, Demo Videos, and more